Nonrigid registration notes:

Previous work:
1. ratio of variance minimisation by Zuo et al: divide each voxel in the transformed image by the corresponding voxel in the reference image. If the images are aligned, a homogenous image is obtained, otherwise it is heterogenous. The algorithm iteratively maximises the homogeneity (i.e. minimises the variance of the ratio between images across all voxels). Limitation: assumes rigid motion

2. Optical flow type algorithm: pyramidal approach, minimises SSD error. The algorithm computes a motion vector u(x,y,z) for each voxel which represents the displacement from the reference image of that voxel. The set of all vectors U is iteratively refined using a Gauss-Netwon method. Assumes intensities in pre and post-enhanced images remain constant.

FFD:
The FFD model is based on cubic B-splines. The B-splines are used instead of Bernstein polynomials because they have local control. This means that a control point only influences its local, surrounding area, which makes the use of large lattices computationally tractable.